## Slide 1
Hardware Architecture — Edge Device Setup
Orange Pi 5 Pro + USB Camera + Supporting Peripherals
Device | Role
Orange Pi 5 Pro (16 GB) | Runs Python, OpenCV, PyTorch, and all 3 AI models locally
USB camera (1080p) | Captures vehicle and license plate at the gate
5V 5A USB-C power supply | Powers Pi under full AI load (weak PSU causes shutdown)
HDMI monitor + keyboard | Setup, testing, and live preview on Pi
Wi-Fi (onboard) | Network connectivity for the edge device
LED / GPIO (optional) | Physical gate open/close indicator
Windows laptop | Record photos/videos; transfer files to Pi via SCP or USB
Design choice: All AI inference runs on Orange Pi (edge AI) — processing stays on device, not in cloud.

## Slide 2
Hardware Connections & Camera Setup
How components are wired and configured on the Pi
Camera placement:
• Live demo on Pi: USB camera → Orange Pi USB port
• Record first, process later: USB camera → laptop → copy to Pi → batch run
Physical layout:
USB Camera → Orange Pi 5 Pro → HDMI → Monitor
Orange Pi ← 5V 5A USB-C PSU | optional GPIO → LED / gate relay
First-time Pi setup:
1. Copy orange_pi_deploy/ to Pi
2. Run setup_orangepi.sh (15–30 min)
3. python download_models.py (~207 MB)
4. python test_models.py
5. Enable NTP for correct timestamps
Preprocessing rule (one line):
Use --preprocess none for clear daylight; --preprocess auto detects weather and runs the matching filter; or force fog/rain/night with --preprocess fog, rain, or night.

## Slide 3
Edge AI Processing on Orange Pi
Three models + weather-aware preprocessing before detection
Model | File | Job
YOLOv8n Plate Detector | plate_best.pt | Find plate bounding box
YOLOv8n Character OCR | char_best.pt | Read plate → ABC-1234
EfficientNet-B4 VMMR | efficientnet_b4_best.pth | 245 vehicle classes
Flag | When to use | Filter applied
--preprocess none | Clear / normal daylight | None (image unchanged)
--preprocess auto | Unknown weather — Pi detects | Clear→none ¦ Fog→defog ¦ Rain→derain ¦ Night→enhance
--preprocess fog | Foggy / hazy images | Defog (Dark Channel Prior)
--preprocess rain | Rainy images | Derain (vertical median + inpaint)
--preprocess night | Low-light / night images | Night enhance (CLAHE + gamma)
Pipeline: Load image → weather preprocess → vehicle classify → plate detect → character OCR → annotated output
Speed on Pi CPU: ~700–1000 ms/image (plate 80–200 ms | OCR 30–100 ms | VMMR 200–800 ms)

## Slide 4
Hardware Demo, Limits & Troubleshooting
Local commands and operational constraints on Pi
Local demo commands:
cd ~/orange_pi_deploy && source venv/bin/activate
python run_webcam.py --camera 0 --preprocess none # clear daylight
python run_webcam.py --camera 0 --preprocess auto # auto-detect weather
python run_images.py recordings/fog/ --preprocess fog
python run_images.py recordings/rain/ --preprocess rain
python run_images.py recordings/night/ --preprocess night
Hardware limits:
• ~1 image/second on CPU (not 30 FPS)
• AI works fully offline on Pi
• Weak PSU causes shutdown — use 5V 5A
• False Fog on clear photos → use --preprocess none
Fixes: 5V 5A PSU | try --camera 1 | enable NTP | fix Windows line endings ($'\r')
Future: GPIO relay board for physical gate motor control