## Slide 1
Hardware Architecture — Edge Device Setup
Orange Pi 5 Pro + USB camera + supporting peripherals
1 / 4
HARDWARE COMPONENTS
Device | Role
Orange Pi 5 Pro (16 GB) | Runs Python, OpenCV, PyTorch, all 3 AI models locally
USB camera (1080p) | Captures vehicle and license plate at the gate
5V 5A USB-C power supply | Required under full AI load — weak PSU causes shutdown
HDMI monitor + keyboard | Setup, testing, and live preview on Pi
Wi-Fi (onboard) | Network connectivity for edge device
LED / GPIO (optional) | Physical gate open/close indicator
Windows laptop | Record media; transfer files to Pi via SCP or USB
Design choice: All AI inference runs on Orange Pi (edge AI) — processing stays on device, not in cloud.

## Slide 2
Hardware Connections & Camera Setup
Wiring, setup steps, and preprocessing selection
2 / 4
CONNECTIONS
Live demo: USB camera → Orange Pi USB port
Record first: camera → laptop → copy to Pi
Layout:
Camera → Orange Pi → HDMI → Monitor
Pi ← 5V 5A PSU | GPIO → LED (optional)
FIRST-TIME SETUP
1. Copy orange_pi_deploy/ to Pi
2. bash setup_orangepi.sh (15–30 min)
3. python download_models.py (~207 MB)
4. python test_models.py
5. Enable NTP for correct timestamps
PREPROCESSING RULE
Use --preprocess none for clear daylight (no filter runs).
Use --preprocess auto to detect weather → runs matching filter automatically.
Force a branch: --preprocess fog (defog) | rain (derain) | night (enhance).
Clear photo → none run | Foggy → defog run | Rainy → derain run | Night → night enhance run.

## Slide 3
Edge AI Processing on Orange Pi
Three models + weather-aware preprocessing before detection
3 / 4
AI MODELS
Model | Job
YOLOv8n Plate | Find plate box
YOLOv8n OCR | Read ABC-1234
EfficientNet-B4 | 245 vehicle classes
PREPROCESS MODES
Flag | Filter
none | Clear — no filter
auto | Detect → apply match
fog | Defog (DCP)
rain | Derain (median)
night | CLAHE + gamma
PI CPU TIMING
Stage | Time
Plate detect | 80–200 ms
Char OCR | 30–100 ms
VMMR | 200–800 ms
Total | 700–1000 ms
PIPELINE FLOW
Load image → weather preprocess → vehicle classify → plate detect → character OCR → annotated output
Key scripts: pipeline.py | preprocessing.py | run_webcam.py | run_images.py
Weather branch runs BEFORE the 3 AI models — same weights used after enhancement.

## Slide 4
Hardware Demo, Limits & Troubleshooting
Local Pi commands and operational constraints
4 / 4
LOCAL DEMO COMMANDS
cd ~/orange_pi_deploy && source venv/bin/activate
python run_webcam.py --camera 0 --preprocess none
python run_webcam.py --camera 0 --preprocess auto
python run_images.py recordings/fog/ --preprocess fog
python run_images.py recordings/rain/ --preprocess rain
python run_images.py recordings/night/ --preprocess night
LIMITS & FIXES
~1 image/sec on CPU (not 30 FPS)
AI works fully offline on Pi
Weak PSU → shutdown — use 5V 5A
False Fog on clear → --preprocess none
Camera error → try --camera 1
Wrong time → enable NTP
Future: GPIO relay for gate motor
PREPROCESS QUICK GUIDE
Daylight / clear dataset → --preprocess none | Unknown weather → --preprocess auto | Known fog/rain/night → force matching flag
Presentation demo: plug camera into Pi → run_webcam.py on HDMI → show ~700–1000 ms inference per frame.